RANK ANALYSIS OF THE ANISOTROPIC INVERSE CONDUCTIVITY PROBLEM

# Juan Felipe P. J. Abascala, William R.B. Lionheartb

# a Departments of Computer Science and Medical Physics, UCL, London, UK

# b Department of Applied Mathematics, UMIST, Manchester, UK

ABSTRACT: Anisotropic conductivity arises in bio-medical EIT, for example in muscle tissue, however the anisotropic inverse conductivity problem can be solved uniquely only up to a diffeomorphism which fixes all points on the boundary. Although a scalar conductivity can be reconstructed from current and voltage measurements, extra information must be provided to uniquely recover the full symmetric tensor field in the anisotropic case. Rank analysis of the sensitivity matrix reveals that fixing the mesh a-priori selects one of the infinity of possible diffeomorphisms, but may lead to a wrong solution. Hence one should not attempt solving the problem for a fixed mesh, and we suggest a procedure to resolve the ambiguity by imposing some constraints which restore uniqueness of the solution.

Keywords: Anisotropy, Dirichlet-to-Neumann mapping, Constraints, Jacobian.

INTRODUCTION

Anisotropic conductivity is present in bio-medical EIT, for example in muscle or bone tissue which are highly anisotropic. The equation that models the electrical potential  in a domain Ω with conductivity  is Laplace’s equation

=0	(1)

where for an anisotropic medium  is a symmetric positive definite tensor field.

The inverse problem is to determine  in  from the Dirichlet-to-Neumann (DtN) mapping or voltage-to-current relation

(2)

where n is the unit outward normal to the surface .

Uniqueness for the isotropic inverse conductivity problem was first proved by Kohn and Vogelius in for real analytic conductivity and extended to piecewise analytic conductivity in . On the other hand, for an anisotropic analytic conductivity the DtN mapping is invariant under a diffeomorphism  from to  fixing points on the boundary , that is , where  is the transformed conductivity under  and is given by the relation

,	(3)

where  is the Jacobian of the diffeomorphism .

The aim of this paper is to analyse numerically the non-uniqueness of the anisotropic inverse problem. We verify the invariance of the DtN mapping  for a finite element (FE) approximation, showing that there are two different conductivities that satisfy the same boundary data. To get a unique solution some constraints must be imposed. Rank analysis of the Jacobian shows that solving the problem for a fixed mesh constrains the problem, if a particular diffeomorphism is selected, and may lead to a wrong solution. From this analysis we suggest a procedure to recover a unique solution by removing  the uncertainty in the diffeomorphism.

MODEL

The forward problem has been solved using a modified version of EIDORS-3D toolkit  which uses first order tetrahedral finite elements. Some changes are necessary to extend isotropic EIDORS-3D for anisotropic media, specifically the representation of the conductivity tensor, the calculation of the system matrix, the Jacobian and the Regularisation matrix .

Since only six conductivity coefficients are independent, we can represent the conductivity tensor as the vector . The Jacobian measures the sensitivity of the voltage measurements to changes in the conductivity. An efficient way to compute the Jacobian (given in ) is to calculate the tensor  for each element  as the tensor product of the driven and the measurement fields (with boundary current patterns  and  respectively)

,	(4)

which has only six independent components so we can denote the Jacobian for each element  by

.	(5)

Each entry is the sensitivity of a voltage measurement with respect to each of the coefficients of . Note that for an isotropic formulation the tensor product in  becomes a scalar product and  a scalar.

To solve the inverse problem using a nonlinear method one may compute on each step the correction on the conductivity as, where is the difference between predicted and measured voltages and  is the regularised inverse of the Jacobian. Therefore, a rank analysis of the Jacobian quantifies how much information is available for the reconstruction of the conductivity. The most reliable way to examine the rank of the Jacobian is the singular value decomposition.

METHODOLOGY

We study the non-uniqueness of the anisotropic inverse problem, first by verifying numerically the invariance of the DtN mapping, and second by looking at the rank of the Jacobian.

The invariance of the DtN mapping was first noted in . The non-injectivity of the DtN mapping can be verified for the FE case by showing that there are two different conductivity distributions  and , related by a diffeomorphism that produce the same voltages at the boundary. It shows that once the mesh is fixed, there is a unique conductivity distribution consistent with the DtN mapping, since fixing the mesh selects one of the infinitely many possible diffeomorphisms. To study the effect of fixing the mesh we look at the rank of the Jacobian for both the isotropic and the anisotropic formulations.

For the rank-analysis, in a -elements mesh we simulate a current injection which consists of  voltage measurements where only  of them are independent. Hence,  is a  matrix for the anisotropic formulation, while for the isotropic case  is a matrix of dimensions . Our rank analysis is performed on the Jacobian by identifying the first large step reduction in the singular values. We denote by the (effective numerical) rank of the Jacobian. This gives the minimum value between  and the number of unknowns that can be recovered from the given noise free data. What we want to show is that while for an isotropic formulation , when , for an anisotropic conductivity we expect .

RESULTS

# 4.1.	Invariance of the DtN mapping

The invariance of the DtN mapping is verified numerically by applying a known diffeomorphism in  and comparing the voltages at the boundary given by  and . Let  be an anisotropic conductivity  defined in a cylindrical mesh FE, the vector of surface voltages V is computed by solving the Forward Problem  such that . The diffeomorphism  is simulated by moving randomly all interior nodes, avoiding a big distortion of the elements and leaving the boundary unchanged, such that we get a new mesh and a known diffeomorphism. The transformed conductivity  is calculated using  for each of the elements. Then, by solving the Forward Problem for  in the new mesh, that is , we get that . Figure 1 shows the voltage difference  for a numerical simulation using an adjacent current pattern with  electrodes.

# Figure 1: Boundary voltage difference

# 4.2.	Rank Analysis. Fixing the mesh

For an isotropic , the number of independent measurements  gives the rank of the Jacobian. The goals of this paper are to analyse  of anisotropic  for a fixed mesh and to estimate the maximum number of unknowns we can recover for an anisotropic conductivity tensor given the DtN mapping.

First, for a spherical mesh of  elements and for an adjacent current pattern, we vary the number of measurements  and calculate  for  by both the isotropic and the anisotropic formulations, where  and  are the ranks calculated by the isotropic and the anisotropic formulation respectively. For ,  and  gives the number of independent measurements , which provides the number of unknowns we can recover. We also calculate  for  a non-homogeneous isotropic matrix and get the same results, so then the rank does not depend on the  values, as we expected. To analyse the effect of fixing the mesh and the ambiguity of the diffeomorphism we must study  for the case , where  is limited by the number of elements , that is, , and  is expected to be in the range . The maximum number of independent measurements that we can get depends on the number and the position of the electrodes, the current pattern, the geometry of the object and the discretisation. We look at  for different values of these parameters for showing the maximum number of unknowns we can recover for a given mesh.  Table 1 shows the maximum  achievable, for a sphere (), a cylinder () and a cube (), by adding as many electrodes as possible, changing their position and implementing opposite and adjacent current-patterns.

Table 1: rI and rA, Jacobian ranks calculated by the isotropic and the anisotropic formulation respectively for isotropic and anisotropic conductivities I and A.

| Geometry | rI(I)/n | rA(I)/n | rA(A)/n |  |  |
| --- | --- | --- | --- | --- | --- |
| Sphere | 1 | 1.73 | 3.1 | 0.71 | 0.33 |
| Cube | 1 | 1.1 | 2.5 | 0.5 | 0.33 |
| Cylinder | 1 | 1.3 | 2.5 | 0.45 | 0.3 |

Having considered different geometries we found that  for anisotropic conductivity , starting from anisotropic conductivity close to isotropic with the calculation of  to non-homogeneous anisotropic conductivity with .

CONCLUSIONS

We have checked first that for a given mesh there is a unique discrete conductivity distribution that agrees with the voltage data and that choosing the mesh is equivalent to selecting a diffeomorphism by representing the conductivity tensor on a particular reference coordinate system.  We have gone on to show that for an anisotropic formulation that the rank of the Jacobian is in the range , when the mesh is fixed. While for the continuous case it is known that we are able to recover the anisotropic tensor only up to a diffeomorphism and then by providing the diffeomorphism we expect to recover the complete conductivity tensor, there is not yet theoretical explanation for piecewise constant conductivity FE case. For the Finite Element case by fixing the mesh we select one of the many possible diffeomorphisms by fixing the position of the vertices, however since there are approximately three times more elements than vertices, then we are not able to recover more than  unknowns.

The problem is that by selecting the mesh we provide information of a specific diffeomorphism, which may lead to a wrong solution since we are selecting a representation on the conductivity that may differ from the physical solution we are interested in. Since the anisotropic inverse conductivity problem is uniquely reconstructed only up to a diffeomorphism fixing the boundary, the idea is to provide a constraint that allows the recovery of the unknown diffeomorphism. We suggest a procedure for resolving the ambiguity in the diffeomorphism and recovering a unique conductivity by imposing some constraints on the solution. First, get an estimate of the conductivity for a fixed mesh, and then find the diffeomorphism that makes  satisfy the constraints.

# REFERENCES

J. F. P. J. Abascal, The anisotropic inverse conductivity problem , M.Sc. Thesis, Manchester University, 2003

R. V. Kohn and M. Vogelius, Determining conductivity by boundary measurements ii. Interior results, Comm. Pure App. Math., 38:643-667, 1985

R. V. Kohn and M. Vogelius, Identification of an unknown conductivity by means of measurements at the boundary, In Proc. SIAM-AMS, Inverse Problems, 14:113-123, 1984.

J. M. Lee and G. Uhlmann, Determining anisotropic real-analytical conductivities by boundary measurements, Comm. Pure App. Math, 38:643-667, 1989.

N. Polydorides and W. R. B. Lionheart, A Matlab tookit for three-dimensional electrical impedance and diffuse optical reconstruction software project, Meas. Sci. Technol., 13:1871-1883, 2002

# Footnotes

j.abascal@cs.ucl.ac.uk